## Slide 1: PDA – PHOTO DIODE ARRAY
CLARITY EXTENSION

## Slide 2: PDA Extension
Spectral data acquisition from selected detectors
Import and export of spectral data in text format
Isoplot and 3D plot for spectral data evaluation
Peak purity evaluation
Spectral library and spectral library search
Overview
PDA Extension / Overview
https://www.dataapex.com/product/extensions-pda

## Slide 3: System Configuration
PDA Extension / System Configuration
PDA option is configured in the System Configuration window
PDA can be enabled on a station where p/n A29 is purchased

## Slide 4: PDA window
PDA Extension / PDA Window
PDA window is accessible from the Chromatogram window
8 different views could be selected in the 4 panes

## Slide 5: PDA Window
Library menu allows you to open or create a new Spectral library.
By default, the Library is stored in the Calib subdirectory of the current Project
Spectral Library pane display details for the spectra in library and allows to display them in Spectral View
Spectral Library
PDA Extension / PDA Window / Spectrum Library

## Slide 6: PDA window
Spectra to the library could be added individually using the Add to Library... command
Multiple spectra could be added from a chromatogram with identified peaks using the Add All Identified Peaks command
Spectral Library
PDA Extension / PDA Window / Spectral Library

## Slide 7: PDA view
Library search results are displayed as an overlay in Spectral View or as a table in Library Search Result
Spectrum search
PDA Extension / PDA View / Spectrum Search

## Slide 8: PDA view
View peak purity for entire chromatogram or a single peak
Spectra for peak start, end, inflection and apex are compared in the Peak Purity Spectra View
Peak purity
PDA Extension / PDA View / Peak Purity

## Slide 9: PDA Method
Peak Purity and Library Search Options are set on the PDA Method tab
Multiple PDA libraries could be set in the method
Measurement Conditions
PDA Extension / PDA Method

## Slide 10: PDA Results
Library search results are displayed as an overlay in Spectral View or as a table in Library Search Result
PDA Name Match belongs to the compound identified by the calibration found in the first PDA library
PDA Best Match Name and PDA Best Match are based on all PDA libraries set in the PDA Method
PDA Extension / PDA Results

## Slide 11: PDA Report
Customize PDA Report to display desired results
PDA Extension / PDA Report

## Slide 12: Export of Graphs
Export graphs into clipboard or save them as a picture (*.emf)
PDA Extension / Export of Graphs

## Slide 13: Thank you for your attention