## Slide 1: DHA – DETAILED HYDROCARBON ANALYSIS
CLARITY EXTENSION

## Slide 2: DHA Extension
Determination of individual components in spark ignition engine fuel
Calculation of % Area/Weight/Volume
  Particular compounds – DHA Results
  Hydrocarbon groups – DHA Group Results (PONA, PIONA, …)
ASTM D-6730
  Preinstalled standard test method
Custom method development
Overview
DHA Extension / Overview
https://www.dataapex.com/product/extensions-DHA

## Slide 3: System Configuration
DHA Extension / System Configuration
DHA Instrument is configured in the System Configuration window
DHA can be enabled on station where p/n A33 is purchased

## Slide 4: Chromatogram Window
DHA Extension / Chromatogram window
DHA tab for specific DHA result calculations

## Slide 5: Settings on the DHA tab
DHA Extension / Settings on the DHA tab
DHA Settings are located on the DHA tab
Create DHA Calibration
Display DHA Result from chromatogram
Edit Link Table: custom compound names

## Slide 6: DHA results
DHA Extension / DHA Results
Shows the calculated results
DHA Method and DHA Calibration from Chromatogram must match with DHA Settings

## Slide 7: DHA Group results
DHA Extension / DHA Group Results
Display Group Results (PIONA, PONA)
Units according to DHA Settings – Corrected Area, % Area, % Weight or % Volume
Selected units are displayed in the table header

## Slide 8: DHA Calibration
DHA Extension / DHA Calibration
Open from DHA Settings – Create DHA Calibration
The standard chromatogram must contain from 6 to 11 calibrated peaks from the n-Paraffins standard sample
Manually enter the measured C1...C4 retention times

## Slide 9: Custom DHA method
DHA Extension / Custom DHA Method
Possibility to adjust DHA Method and Calibration according to your needs
Develop method based on a specific laboratory instrumentation

## Slide 10: Thank you for your attention