## Slide 1: Clarity training
Advanced – part 1

## Slide 2: agenda
Instrument window
  User Options
Single Analysis
  Injected volume
  Autosampler use
Sequence table
  Sequence Mode
  Options
  Import, Fill series
ADVANCED TRAINING

## Slide 3: agenda
Instrument window
  User Options
Single Analysis
  Injected volume
  Autosampler use
Sequence table
  Sequence Mode
  Options
  Import, Fill series
ADVANCED TRAINING

## Slide 4: INSTRUMENT WINDOW
Stored in desktop *.dsk files = can be set individually for each user
Shared desktop file to share settings
USER OPTIONS
ADVANCED TRAINING / INSTRUMENT WINDOW / USER OPTIONS

## Slide 5: Single analysis
Linear detector response is considered
First, set Default Injected Volume in Calibration Options
In Single Analysis, set the Injection volume for the sample and standard
The responses are corrected by the ratio of Inj. Volume and Default Injected Volume in recalibration or calibration calculations
INJECTED volume
ADVANCED TRAINING / SINGLE ANALYSIS / INJECTED VOLUME

## Slide 6: Single analysis
Inject & Run performs one injection from the specified vial and starts the acquisition
Vial can be selected via a graphic interface if supported by the AS
The Use Autosampler checkbox is present only if AS is configured
Autosampler use
ADVANCED TRAINING / SINGLE ANALYSIS / AUTOSAMPLER USE

## Slide 7: agenda
Instrument window
  User Options
Single Analysis
  Injected volume
  Autosampler use
Sequence
  Description
  Options and functions overview
  Import, Fill series, Select vial
ADVANCED TRAINING

## Slide 8: SEQUENCE TABLE OVERVIEW
Samples are added by filling the last empty row
  When any field is filled, the other fields are copied from the previous row
Copy & Paste one or more rows to add samples
Import of sample data from text files
Reprocessing of the last measured sample set
ADD SAMPLES
ADVANCED TRAINING / SEQUENCE TABLE OVERVIEW / ADD SAMPLES

## Slide 9: Sequence window
SV, EV = start and end vial injection number
  A single row can define several vials/injections
Sample Type, Lvl = can be used for automatic recalibration via sequence
Window bottom shows the state of the sequence (runtime, vial, etc.)
Description
ADVANCED TRAINING / SEQUENCE WINDOW / DESCRIPTION

## Slide 10: Sequence window
Run sequence using Ctrl+Q or the icon
  Running sequence will lead to a reset of all rows (indicated by a message dialog)
Resume sequence Ctrl+Space or the icon
  Continue from the first unmeasured row with the Run option checked
Tooltips display additional details (e.g., actual file names of measured chromatograms, etc.)
Description
ADVANCED TRAINING / SEQUENCE WINDOW / DESCRIPTION

## Slide 11: SEQUENCE WINDOW
Snapshot : create a temporary snapshot (will be replaced by the complete chromatogram when measured)
Abort sequence : terminate the sequence without saving the current chromatogram
Stop sequence : 1st click halts the sequence after the current measurement, 2nd click stops analysis immediately
Repeat injection : interrupt the actual measurement and repeat injection
Skip vial
Check sequence for errors
Basic functions
ADVANCED TRAINING / SEQUENCE WINDOW / BASIC FUNCTIONS

## Slide 12: SEQUENCE WINDOW
Useful file name variables: %s = sequence, %J = Method, %P = project, %Q = Sample
Bypass sample type = run without injection (for startup and shutdown methods)
Include in SST – perform SST test when injection is finished
Stored Calib. – chromatogram will be opened with stored calibration
Close All – close all currently opened chromatograms in overlay
Basic functions
ADVANCED TRAINING / SEQUENCE WINDOW / BASIC FUNCTIONS

## Slide 13: SEQUENCE WINDOW
Passive sequence: Clarity only expects the START signal, the time of analysis is set by the autosampler (AS)
Active sequence: Clarity sends a READY signal to the AS and waits for the START signal
  AS control in active sequence: AS injects according to SV, EX, I/V, and Inj. Volume in the Sequence Table
Set the initial value for the %n variable
Choose the calibration mode applied for the whole sequence
SEQUENCE MODES AND OPTIONS
ADVANCED TRAINING / SEQUENCE WINDOW / SEQUENCE MODES AND OPTIONS

## Slide 14: SEQUENCE WINDOW
Import Sequence Step 1 dialog: select files to import
Import Sequence Step 2 dialog: assign the respective fields to be imported
  the Start Vial (SV) and File Name (both in bold) are mandatory
IMPORT
ADVANCED TRAINING / SEQUENCE WINDOW / IMPORT

## Slide 15: SEQUENCE WINDOW
Available in Sequence and Calibration
Select a cell to be used for filling (numeric inputs, text inputs with numeric counters)
Fill down (Ctrl+F):
  Fill the cells below with the parameter in the selected cell
Fill series:
  Open the Fill Series dialog and specify the fill/replace parameters
FILL SERIES AND FILL DOWN
ADVANCED TRAINING / SEQUENCE WINDOW / FILL SERIES AND FILL DOWN

## Slide 16: SEQUENCE WITH AUTOSAMPLERS
The dialog with a graphic interface can be opened from Single Analysis/Sequence or viewed in Method Setup
Convenient for working with autosamplers (available only in some AS)
For controlled autosamplers, the vial number and injection volume are set in this dialog
Allows mid-run modifications for not yet processed samples
Select vial
ADVANCED TRAINING / SEQUENCE WITH AUTOSAMPLERS / SELECT VIAL

## Slide 17
Short break