## Slide 1: Clarity training
Basic operations

## Slide 2: content
Developing a method
Acquiring data
  Single Analysis
  Sequence
Creating calibration
Quantifying results
Reporting results
BASIC OPERATIONS / CONTENT
Notes: During this training session, we will be looking at the different basic tasks that Clarity can perform.
These are: Developing a Method, acquiring data, Creating a calibration file and Reporting of Data.
This session will be addressed from the point of view of a first-time user of the Clarity Chromatography Station.

## Slide 3: Method in clarity
Instrumental and processing parameters within one document
Can be sent to HW directly from Method Setup
Stored as *.met file in current project folder
BASIC OPERATIONS / METHOD

## Slide 4: Method development
Set acquisition parameters
Enter sample information (optional)
Acquire the first chromatogram
Optimize integration parameters
Store the method for further analyses
BASIC OPERATIONS / METHOD DEVELOPMENT
Proposed workflow

## Slide 5: Method development
Accessed from Instrument window
Available tabs are dependent on used configuration
BASIC OPERATIONS / METHOD DEVELOPMENT / METHOD SETUP
Method setup

## Slide 6: Method setup
Description
  Informative
Autostop & Run time
External Start/Stop
BASIC OPERATIONS / METHOD DEVELOPMENT / METHOD SETUP / MEASUREMENT TAB
Measurement tab

## Slide 7: Method setup
Device-specific
Cannot be modified during acquisition
“Enabled” checkbox
BASIC OPERATIONS / METHOD DEVELOPMENT / METHOD SETUP / ACQUISITION TAB
acquisition tab

## Slide 8: Method setup
Signal out of range = loss of information
BASIC OPERATIONS / METHOD DEVELOPMENT / METHOD SETUP / ACQUISITION TAB / SIGNAL RANGE
Signal range

## Slide 9: Method setup
Too low = not enough datapoints per peak = incorrect results
“Correct” rate is dependent on HW and analytical application
  GC detectors – usually 25-50 Hz
  LC and Spectral detectors – according to application and HW parameters
BASIC OPERATIONS / METHOD DEVELOPMENT / METHOD SETUP / ACQUISITION TAB / SAMPLE RATE
SAMPLE RATE
Low Sample Rate

## Slide 10: Method setup
Parameters are applied to measured chromatograms
Selection of integration algorithm
Integration table is separate for each signal
BASIC OPERATIONS / METHOD DEVELOPMENT / METHOD SETUP / INTEGRATION TAB
integration tab

## Slide 11: Method setup
Global parameters
  Peak width, Threshold, Bunching, Slope
Integration Interval
Other interval and peak functions
BASIC OPERATIONS / METHOD DEVELOPMENT / METHOD SETUP / INTEGRATION TAB / INTEGRATION PARAMETERS
integration parameters
Threshold
Peak width

## Slide 12: Method setup
Calibration that is linked to measured chromatograms
Calculation type
Calibration cloning
BASIC OPERATIONS / METHOD DEVELOPMENT / METHOD SETUP / CALCULATION TAB
Calculation tab

## Slide 13: Method development
BASIC OPERATIONS / METHOD DEVELOPMENT / SINGLE ANALYSIS
SINGLE ANALYSIS – FIRST RUN

## Slide 14: Single analysis
BASIC OPERATIONS / METHOD DEVELOPMENT / SINGLE ANALYSIS / ANALYSIS
Analysis tab
Enter sample information
Enter file name
  Use variables by clicking

## Slide 15: Single analysis
BASIC OPERATIONS / METHOD DEVELOPMENT / SINGLE ANALYSIS / POST RUN
Post run settings tab
Automatic operations after the end of analysis

## Slide 16: Single analysis
BASIC OPERATIONS / METHOD DEVELOPMENT / SINGLE ANALYSIS / SENDING METHOD
Sending method

## Slide 17: Method development
BASIC OPERATIONS / METHOD DEVELOPMENT / DATA ACQUISITION
Data acquisition

## Slide 18: Data acquisition
BASIC OPERATIONS / METHOD DEVELOPMENT / DATA ACQUISITION
Monitoring analysis
Functions
  Snapshot – Temporary chromatogram
  Abort – End analysis, no chromatogram saved
  Stop – End analysis, save chromatogram
Parameters – Only influence view, not data itself

## Slide 19: Method development
BASIC OPERATIONS / METHOD DEVELOPMENT / CHROMATOGRAM
FIRST CHROMATOGRAM
Optimize integration
  Global parameters
  Integration interval
  Other functions
Change integration algorithm
Global parameters
Modify peaks
Integration parameters
Modify baseline

## Slide 20: Method development
BASIC OPERATIONS / METHOD DEVELOPMENT / CHROMATOGRAM
FIRST CHROMATOGRAM
Signal Scailing – Focus on relevant peaks before integration tuning

## Slide 21: Chromatogram
BASIC OPERATIONS / METHOD DEVELOPMENT / CHROMATOGRAM
Saving optimized method
Save as method – saves settings from a chromatogram to new method
  Instrumental part
  Integration
  Linked calibration
  Etc.

## Slide 22: sequence
BASIC OPERATIONS / SEQUENCE
Analyze many samples using autosampler
  Can be used with manual injection
Utilize optimized method from previous steps

## Slide 23: sequEnce
Sequence table 1/3
BASIC OPERATIONS / SEQUENCE / SEQUENCE TABLE
Status
Vial information
Sample information
Values for additional calculations
Injection volume – important for autosampler

## Slide 24: sequEnce
Sequence table 2/3
BASIC OPERATIONS / SEQUENCE / SEQUENCE TABLE
File name – usable variables
Sample type (+ Levels for standards)
Acquisition and printing methods
Automated post run actions

## Slide 25: sequEnce
Sequence table 3/3
BASIC OPERATIONS / SEQUENCE / SEQUENCE TABLE
Hidden columns – setup columns dialog
  Accessible from local menu
  Applicable to most tables in Clarity

## Slide 26: Calibration
BASIC OPERATIONS / CALIBRATION
Stored as *.cal files
Identification of compounds based on retention time

## Slide 27: Calibration
Manual creation
BASIC OPERATIONS / CALIBRATION / MANUAL CREATION
Acquire and integrate standard samples
Set calibration options
Add (concentration) levels
Save calibration
Link it to chromatograms
Open Standard
Add Peaks
Enter Compounds‘ Names
(1st time only)
Enter Amounts

## Slide 28: Calibration
Calibration options
BASIC OPERATIONS / CALIBRATION / CALIBRATION OPTIONS
Display mode – ESTD, ISTD etc.
Calibration
  Automatic – recommended
  Manual – addition of each peak requires manual confirmation
Mode
  Calibrate – peaks added to first empty level
  Recalibrate – peaks applied to selected level
Recalibration
  Replace – only uses last measured response
  Average – uses averaged response from “x” measurements
Compound units
  Displayed in result table

## Slide 29: calibration
Filling level 1/4 - opening standard
BASIC OPERATIONS / CALIBRATION / FILLING LEVEL

## Slide 30: calibration
Filling level 2/4 - Adding peaks
BASIC OPERATIONS / CALIBRATION / FILLING LEVEL

## Slide 31: calibration
Filling level 3/4 – naming compounds (1st level only)
BASIC OPERATIONS / CALIBRATION / FILLING LEVEL

## Slide 32: calibration
Filling level 4/4 – filling amounts
BASIC OPERATIONS / CALIBRATION / FILLING LEVEL

## Slide 33: calibration
Next level
BASIC OPERATIONS / CALIBRATION / NEXT LEVEL
Repeat the previous steps for each level
Use “Calibration” settings
  New peaks added to empty level

## Slide 34: calibration
saving
BASIC OPERATIONS / CALIBRATION / SAVING

## Slide 35: calibration
Individual compound tabs
BASIC OPERATIONS / CALIBRATION / COMPOUND TAB
Details for the given compound
Overview of all levels
How identified
How quantified
Calibration curve graph

## Slide 36: calibration
Linking to chromatogram
BASIC OPERATIONS / CALIBRATION / LINK TO CHROMATOGRAM
Calibration from method is automatically linked to all measured chromatograms

## Slide 37: reports
WHERE TO ENABLE/EXECUTE
BASIC OPERATIONS / REPORTS
Manually from given window
Automatically after analysis end
Batch dialog

## Slide 38: reports
Report setup
BASIC OPERATIONS / REPORTS
“Printing method” set separately for each window
*.sty files in COMMON folder

## Slide 39: Thank you for your attention